## Slide 1
WEEK 2 - LECTURE 2
Computer Vision for Warehouse Robots
Giving Robots the Gift of Sight
Course: Introduction to Robotics for AI and Data Science
Instructor: Dr. Akram Fatayer
linkedin.com/in/akram-fatayer
Institution: Al-Zaytoonah University of Jordan

## Slide 2
The Warehouse Robot Challenge
Your warehouse robot has a mission: locate and retrieve a specific red box among hundreds of items.
Human Approach
Look around the warehouse, visually scan for red objects, recognize the target box, navigate to it.
Current Robot
Can move around the warehouse, but cannot see or identify objects. It's essentially blind.
The Problem: How do we give the robot the ability to perceive and understand its visual environment?

## Slide 3
Why Computer Vision is Critical for Robotics
$214B
Global Robotics Market by 2030
80%
Of Robots Need Vision Systems
$50B+
Warehouse Automation Market
Real-World Applications
Warehouse Automation
Amazon, FedEx: Item picking, sorting, inventory management
Autonomous Vehicles
Tesla, Waymo: Object detection, lane keeping, navigation
Manufacturing
Quality inspection, assembly guidance, defect detection
Agriculture
Crop monitoring, fruit picking, precision farming

## Slide 4
Breaking Down the Vision Problem
Complex problems become manageable when decomposed into steps
1
Image Capture
Get raw pixels from camera sensor
2
Image Processing
Filter, enhance, transform color spaces
3
Object Detection
Find regions containing objects
4
Recognition
Classify what each object is
5
3D Localization
Estimate position in 3D space
Each step uses techniques you already know from AI/DS: data preprocessing, feature extraction, classification,
regression

## Slide 5
Cameras as Data Sensors
1. Lens System
Focuses incoming light rays from the 3D world onto a 2D sensor plane. Controls field of view and depth of field.
2. Sensor Array
Grid of photodetectors (pixels) that convert photons into electrical signals. Each pixel measures light intensity.
3. Color Filters
Bayer filter pattern separates light into Red, Green, Blue channels. Three measurements per pixel location.
Data Output
Image: H × W × 3 array
Each pixel stores [R, G, B] values (0-255) Example: 640×480 image = 921,600 numbers

## Slide 6
Camera Parameters and Trade-offs
Choosing the right camera configuration for robotic applications
Parameter
Description
Benefit
Trade-off
Resolution
Number of pixels (e.g., 640×480, 1920×1080)
Higher detail, better object recognition
More computation, slower processing
Frame Rate
Images per second (e.g., 30 FPS, 60 FPS)
Smoother tracking, faster response
Higher bandwidth, more processing load
Field of View
Angular extent of observable world (narrow vs. wide)
Wide: see more area
Narrow: more detail
Wide: distortion
Narrow: limited context
Focal Length
Distance from lens to sensor (short vs. long)
Long: zoom capability
Short: wider view
Long: narrow FOV
Short: less detail
For warehouse robots: Balance is key — 640×480 at 30 FPS with moderate FOV provides good performance without overwhelming the processor

## Slide 7
From 3D World to 2D Image
Pinhole Camera Model
Light rays from 3D points pass through a single point (optical center) and project onto the image plane. This creates perspective projection.
Perspective Projection
Objects farther away appear smaller. Parallel lines converge to vanishing points. This is how humans see the world too.
x_image = f × (X_world / Z_world)
The Fundamental Challenge
Depth information is lost! A 2D point in the image could correspond to any 3D point along a ray. We need additional information (stereo vision, depth sensors, or learned priors) to recover 3D structure.

## Slide 8
Images as Data: The AI/DS Perspective
Images are just structured numerical arrays — familiar territory for data scientists
Array Representation
shape: (480, 640, 3)
dtype: uint8 (0-255)
size: 921,600 values
# Load image as NumPy array import cv2 import numpy as np img = cv2.imread('robot_view.jpg') print(img.shape) # (480, 640, 3) # Access pixel at row 100, col 200 pixel = img[100, 200] # [R, G, B] # Slice region of interest roi = img[100:200, 150:250] # Apply operations (just like any array) mean_color = np.mean(img, axis=(0,1))
Key Insights
Images are 3D arrays: Height × Width × Channels
Use familiar tools: NumPy, PyTorch, Pandas
Same operations: slicing, indexing, broadcasting
Computer vision = structured data processing

## Slide 9
Color Spaces: RGB vs HSV
RGB Color Space
Red, Green, Blue — How cameras capture light
Three channels: R, G, B (0-255 each)
Mixes color and brightness together
Same red appears different in shadow vs. sunlight
Hard to define "red" with simple thresholds
Problem: Sensitive to lighting variations
HSV Color Space
Hue, Saturation, Value — How humans perceive color
Hue:
The actual color (0-180°)
Saturation:
Color intensity (0-255)
Value:
Brightness (0-255)
Separates color from lighting conditions
Why HSV for Robotics?
Warehouse lighting changes throughout the day. HSV allows us to detect "red objects" regardless of whether they're in bright light or shadow — just threshold the Hue channel!

## Slide 10
Color-Based Detection Pipeline
1
RGB → HSV
Convert image to HSV color space
2
Threshold
Create binary mask for target color range
3
Morphology
Clean noise with erosion and dilation
4
Find Contours
Detect connected regions in mask
5
Bounding Box
Draw rectangles around detected objects
# Complete color detection pipeline hsv = cv2.cvtColor(image, cv2.COLOR_BGR2HSV) mask = cv2.inRange(hsv, lower_red, upper_red) mask = cv2.morphologyEx(mask, cv2.MORPH_OPEN, kernel) contours, _ = cv2.findContours(mask, cv2.RETR_EXTERNAL, cv2.CHAIN_APPROX_SIMPLE) # Draw bounding boxes for contour in contours: x, y, w, h = cv2.boundingRect(contour) cv2.rectangle(image, (x,y), (x+w,y+h), (0,255,0), 2)
Advantages
Fast and simple to implement
Works well for distinct colors
No training data needed
Limitations
Sensitive to lighting changes
Cannot recognize object types
Fails with similar colors

## Slide 11
CNNs Learn Visual Features
Hierarchical Feature Learning
Layer 1
Edges
Layer 2-3
Textures
Layer 4-5
Parts
Layer 6+
Objects
Why CNNs Work
CNNs automatically learn relevant features from data instead of requiring hand-crafted feature engineering. Early layers detect simple patterns (edges), deeper layers combine them into complex representations (objects).
Convolutional Layers
Apply learned filters across the image. Each filter detects a specific pattern. Spatial structure is preserved, unlike fully-connected layers.
Pooling Layers
Reduce spatial dimensions while keeping important features. Provides translation invariance — object detected regardless of exact position.
Connection to Your ML Knowledge
Same backpropagation training
Same loss functions (cross-entropy)
Same optimization (SGD, Adam)
Just different architecture!

## Slide 12
Object Detection for Robotics
Two-Stage Detectors
Examples:
R-CNN, Faster R-CNN
Step 1: Propose regions
Step 2: Classify each region
Higher accuracy
Slower inference (2-5 FPS)
Accuracy
High
Speed
Slow
One-Stage Detectors
Examples:
YOLO, SSD, MobileNet
Single pass through network
Predict boxes and classes together
Good accuracy
Fast inference (30+ FPS)
Accuracy
Good
Speed
Fast
For Warehouse Robots: Use One-Stage Detectors
Real-time performance is critical. We'll use MobileNet-SSD (lightweight, fast) and YOLO (more accurate) in the lab. Both run at 30+ FPS on modest hardware.

## Slide 13
Transfer Learning: From COCO to Warehouse
Pre-training
Model trained on large dataset (ImageNet: 1M images, COCO: 330K images) learns general visual features
Transfer
Use pre-trained weights as starting point. Early layers (edges, textures) transfer well across domains
Fine-tuning (Optional)
Train on warehouse-specific data to adapt to your domain. Only needed if pre-trained model insufficient
Why Transfer Learning?
No need to collect millions of training images
Faster training (hours instead of weeks)
Better performance with limited data
Leverages knowledge from large datasets
In Practice
Download pre-trained MobileNet-SSD or YOLO
Use directly for common objects (boxes, people)
Fine-tune if detecting custom objects
Same concept from your ML course!

## Slide 14
Deploying CNNs on Robots
Robots have limited compute power, memory, and battery — we need efficient models
Model
Size
Speed (FPS)
Accuracy (mAP)
Use Case
ResNet-101
170 MB
5 FPS
76%
Cloud/Server
YOLOv5
28 MB
45 FPS
65%
Desktop/Laptop
MobileNet-SSD
6 MB
60 FPS
60%
Embedded/Robot
TinyYOLO
4 MB
80 FPS
55%
Microcontroller
Efficient Architectures
MobileNet, EfficientNet use depthwise separable convolutions to reduce parameters while maintaining accuracy
Model Quantization
Convert 32-bit floats to 8-bit integers. 4× smaller, 2-4× faster, minimal accuracy loss
Edge AI Accelerators
Google Coral TPU, NVIDIA Jetson, Intel Neural Compute Stick provide hardware acceleration

## Slide 15
Object Tracking for Navigation
Tracking maintains object identity across frames — more efficient than detecting from scratch each time
Detection Only
Run CNN on every frame independently. No memory of previous frames.
Pros: Simple, no state management
Cons: Computationally expensive, no temporal consistency, ID switching
Detection + Tracking
Detect occasionally, track between detections. Predict object location based on motion.
Pros: Faster, stable IDs, motion prediction
Cons: More complex, can lose track
Centroid Tracking
Match objects by distance between centroids in consecutive frames. Simple but effective.
Use: Slow-moving objects
Kalman Filter
Predict next position using motion model. Optimal for linear motion with Gaussian noise.
Use: Predictable trajectories
DeepSORT
Combines appearance features (CNN) with motion (Kalman). Handles occlusions well.
Use: Complex scenarios
Warehouse Robot Application
Track target item as robot approaches. Detect every 10 frames, track in between. Predict item location if temporarily occluded. Maintain stable ID for grasping system.

## Slide 16
Computer Vision as Machine Learning
Generic ML
Data
Tabular, text, time series
Preprocessing
Normalization, encoding
Model
Neural net, tree, SVM
Evaluation
Accuracy, F1, AUC
Computer Vision
Data
Images (H×W×3 arrays)
Preprocessing
Resize, augment, normalize
Model
CNN (ResNet, YOLO)
Evaluation
mAP, IoU, precision
Same Concepts, Different Data Type
Everything you learned in ML applies to CV: train/val/test splits, overfitting, regularization, transfer learning, hyperparameter tuning. Images are just high-dimensional structured data!
Data
NumPy arrays, PyTorch tensors
Training
Same optimizers (Adam, SGD)
Loss
Cross-entropy, MSE, IoU
Frameworks
PyTorch, TensorFlow, Keras

## Slide 17
Sim-to-Real Gap in Vision
Simulation (PyBullet)
Perfect lighting, no shadows
Clean textures, no noise
Ideal camera (no distortion, blur)
Consistent colors
No occlusions or clutter
Real World
Variable lighting, shadows, reflections
Sensor noise, motion blur
Lens distortion, chromatic aberration
Color variations (manufacturing, wear)
Background clutter, occlusions
Bridging the Gap
Domain Randomization
Vary lighting, textures, colors in simulation. Train on diverse conditions so model generalizes better to real world.
Realistic Rendering
Use physics-based rendering with shadows, reflections, noise. Makes simulation closer to reality.
Real-World Fine-tuning
Train in sim, collect small real dataset, fine-tune. Combines sim efficiency with real-world accuracy.
In This Course
Weeks 1-3: Develop algorithms in PyBullet simulation. Week 4+: Test on real hardware (Raspberry Pi camera, Arduino). Experience the sim-to-real challenge firsthand and learn to adapt!

## Slide 18
Week 2 Lab: Computer Vision for Warehouse Robot
1
Camera Setup
Configure virtual camera in PyBullet. Capture and display RGB images from robot's perspective.
25 points
2
Color Detection
Implement HSV-based color detection. Detect and localize colored objects in warehouse scene.
30 points
3
CNN Detection
Use MobileNet-SSD and YOLO for object detection. Compare performance and accuracy.
30 points
Deliverables
Python code files (all parts)
Screenshots showing detection results
Lab report (3-5 pages) answering questions
Comparison analysis (color vs CNN)
Timeline & Support
Due: Next class (1 week) Lab Hours: TBD for hands-on help Starter Code: Available on GitHub Office Hours: For questions and debugging

## Slide 19
Warehouse Robot Project Progress
Module 1: Basics
Robot simulation, motion control, sensor reading
✓ COMPLETED
Module 2: Vision
Camera setup, object detection, visual perception
▶ CURRENT
Module 3: LIDAR
Distance sensing, obstacle detection, mapping
UPCOMING
Module 4: Navigation
Path planning, obstacle avoidance, autonomous movement
UPCOMING
Capability Added This Week
Your warehouse robot can now see and recognize objects using its camera! It can detect items by color or use deep learning to identify specific object types. This is the foundation for autonomous item retrieval.
Next Week: LIDAR and Sensor Fusion
We'll add distance sensing to complement vision. Learn how to combine camera and LIDAR data for robust perception in cluttered warehouse environments.

## Slide 20
Key Takeaways
1
Computer vision is critical for autonomous robots
80% of robots need vision systems. Cameras provide rich information about the environment for perception and decision-making.
2
Break complex problems into manageable steps
Vision pipeline: capture → process → detect → recognize → localize. Each step builds on the previous one.
3
HSV is better than RGB for robotic applications
HSV separates color from brightness, making detection robust to lighting variations in real-world environments.
4
CNNs learn hierarchical visual features automatically
Early layers detect edges, deeper layers combine them into objects. Transfer learning lets us use pre-trained models.
5
Real-time performance requires efficient models
MobileNet and YOLO provide good accuracy at 30+ FPS. Trade-offs between model size, speed, and accuracy.
6
Computer vision is just another ML problem
Same concepts you know: training, validation, overfitting, transfer learning. Images are structured data arrays!

## Slide 21
Questions?
Email: a.fatayer@zuj.edu.jo
Office Hours: email me to book a meeting
linkedin.com/in/akram-fatayer
Thank you!
Dr. Akram Fatayer • AI and Data Science Department Al-Zaytoonah University of Jordan