## Slide 1
INTRODUCTION TO ROBOTICS FOR AI & DATA SCIENCE
Lab 1: Hello, Robot! Your First Step to Autonomy
Implementation Guide & Code Walkthrough
Dr. Akram Fatayer
Al-Zaytoonah University of Jordan
a.fatayer@zuj.edu.jo
linkedin.com/in/akram-fatayer/

## Slide 2
This Lab Builds the Foundation of Your Autonomous System
The Primitives of Autonomy
By the end of today, you will have a robot that can: spawn in a simulation, read its own state, and move in a controlled pattern.
Sense & Act
This lab establishes the "Sense" and "Act" components of the Sense-Plan-Act cycle. Everything we do from now on builds upon this foundation.
Real-World Relevance
These are the exact same primitive operations used in real autonomous vehicles, drones, and industrial robotic arms.
Lab 1: Hello, Robot!
Block 1: Perception

## Slide 3
Each Student Creates a Unique, Isolated Conda Environment
Why Unique Environments?
Shared lab computers mean shared conflicts. Creating your own environment ensures your code runs exactly the same way every time, unaffected by other students' changes.
Why conda-forge?
Conda manages both Python and non-Python dependencies together. The conda-forge channel provides the most reliable, up-to-date scientific packages (like PyBullet).
The Golden Rule
Always try
conda install
first. Only use
pip install
as a fallback if a package is not available on Conda.
bash - conda setup
# 1. Create your unique environment (Do this ONCE)
$ conda create -n robotics_Ahmad python=3.11 -y
# 2. Activate it (Do this EVERY TIME you open a terminal)
$ conda activate robotics_Ahmad
# 3. Install required packages from conda-forge
(robotics_Ahmad) $ conda install -c conda-forge pybullet numpy matplotlib opencv -y
Lab 1: Hello, Robot!
Block 1: Perception

## Slide 4
Four Scripts, Four Skills, One Complete Foundation
Incremental Integration
Each script builds directly on the previous one. You start by creating the world, then sensing it, acting within it, and finally analyzing your performance. This is the core methodology of the course.
Automated Self-Grading
Plus:
check_my_lab.py
Before submission, run this script to get instant feedback. It
verifies your robot's trajectory, reinforcing test-driven
development principles.
Lab 1: Hello, Robot!
Block 1: Perception

## Slide 5
spawn_robot.py: Five Steps to Create a Simulated World
1
Connect to Physics Engine
Use
p.GUI
for visual, or
p.DIRECT
for headless.
2
Set Search Path
Tell PyBullet where to find
plane.urdf
and
r2d2.urdf
.
3
Set Gravity
Establish gravity (Z = -9.8 m/s²).
4
Load URDF Models
Load robot & plane URDFs to the world.
5
Run Simulation Loop
Advance the physics one step at a time.
Expected Output:
A GUI showing R2D2 on a plane.
spawn_robot.py
import
pybullet
as
p
import
pybullet_data
# 1. Connect
p.
connect
(p.GUI)
# 2. Search path
p.
setAdditionalSearchPath
(pybullet_data.
getDataPath
())
# 3. Gravity
p.
setGravity
(0,0,-9.8)
# 4. Load URDFs
p.
loadURDF
("plane.urdf")
p.
loadURDF
("r2d2.urdf", [0,0,0.1])
# 5. Run loop
for _ in range(1200):
p.
stepSimulation
()
Lab 1: Hello, Robot!
Block 1: Perception

## Slide 6
read_sensors.py
: Teaching Your Robot to "Feel" Its Own State
Proprioceptive Sensing
Sensing the robot's own internal state (position, orientation, speed). This is how the robot knows where its body is in space.
Exteroceptive Sensing
Sensing the external world (cameras, lidar, ultrasonic). We will cover this in future labs when we add "eyes" to the robot.
The Golden Rule
You cannot control what you cannot measure. Before we can make the robot move accurately, we must be able to read its current state.
pos, orn = p.getBasePositionAndOrientation(robotId)
Returns the (x, y, z) position and the orientation as a quaternion (x, y, z, w).
lin_vel, ang_vel = p.getBaseVelocity(robotId)
Returns linear velocity (vx, vy, vz) and angular velocity (wx, wy, wz).
euler = p.getEulerFromQuaternion(orn)
Converts complex quaternions into human-readable (roll, pitch, yaw) angles.
Expected Console Output (Every 0.5s)
Time: 2.50s
Position (x,y,z): (0.000, 0.000, 0.500)
Orientation (r,p,y): (0.000, 0.000, 0.000)
Linear Velocity: (0.000, 0.000, 0.000)
Angular Velocity: (0.000, 0.000, 0.000)
Lab 1: Hello, Robot!
Block 1: Perception

## Slide 7
move_robot.py: Commanding Motion with resetBaseVelocity
The Core Function
import pybullet as p # Directly sets the robot body's velocity p.resetBaseVelocity(robotId, linearVelocity=[vx, vy, 0], angularVelocity=[0, 0, wz])
This function directly commands the robot's base. It is simple, reliable, and perfect for learning the fundamentals of motion control before dealing with complex wheel physics.
The Body-to-World Frame Problem
Robot thinks: "Move forward/backward" (Body Frame)
Physics engine thinks: "Move along X/Y/Z" (World Frame)
Solution: Use the current yaw angle to convert: vx = speed * cos(yaw), vy = speed * sin(yaw)
Movement Parameters (2x2m Square)
1.0 m/s
LINEAR SPEED
2.0 s
MOVE DURATION
π/2 rad/s
TURN SPEED (90°/S)
1.0 s
TURN DURATION
The Control Loop
To draw a square, we repeat the sequence 4 times:
For i in range(4)
Move Forward (2s)
Turn Left (1s)
Expected Output: The robot traces a visible square in the GUI window and returns to its starting position.
Lab 1: Hello, Robot!
Block 1: Perception

## Slide 8
Why cos(yaw) and sin(yaw)? Converting Body Frame to World Frame
The Core Problem
The robot thinks in "forward/backward" (Body Frame), but the physics engine thinks in absolute "X/Y/Z" coordinates (World Frame).
The Trigonometric Solution
We use the robot's current heading (
yaw
) to convert its
forward speed into global X and Y velocities:
Facing East (yaw=0): vx = speed × cos(0) = speed vy = speed × sin(0) = 0
Key Insight
The robot's "forward" direction changes as it turns, but the world's X and Y axes stay fixed. This is why we must recalculate vx and vy at every simulation step.
Lab 1: Hello, Robot!
Block 1: Perception

## Slide 9
visualize_trajectory.py: From Raw Data to Actionable Insights
Step 1: Data Logging
Instead of just watching the robot move, we need to record its position at every step to analyze its performance later.
# Initialize empty list trajectory = [] # Inside simulation loop: pos, _ = p.getBasePositionAndOrientation(robotId) trajectory.append([pos[0], pos[1], pos[2]])
Headless Mode (p.DIRECT)
When collecting data, we don't need the GUI. Using p.DIRECT runs the simulation thousands of times faster in the background.
Step 2: Plotting with Matplotlib
We convert the list into a NumPy array and plot the X and Y coordinates to visualize the path.
import matplotlib.pyplot as plt import numpy as np traj_array = np.array(trajectory) plt.plot(traj_array[:, 0], traj_array[:, 1]) plt.show()
Generates a 2D Top-Down View of the Square Path
Lab 1: Hello, Robot!
Block 1: Perception

## Slide 10
Verify Your Work Before Submission
Automated Testing
In industry, code is never deployed without automated
tests. We introduce this concept in Lab 1 with the
check_my_lab.py
script.
What It Checks
Shape: Did the robot make exactly 4 turns?
Distance: Are the sides approximately 2 meters long?
Closure: Did the robot return to its starting point?
Instant Feedback
Run this script as many times as you need. If all tests pass, you are guaranteed full marks for the coding portion of the lab.
Terminal
(robotics) user@zuj:~$ python check_my_lab.py
--- Running Automated Lab Check for Week 1 ---
Importing your 'move_square' function...
Running simulation in background...
[PASS] 4 Corners Detected
Found exactly 4 distinct turning points.
[PASS] Side Lengths are ~2m
Measured sides: ['2.01', '1.98', '2.03', '1.99']
[PASS] Returned to Origin
Final distance from start: 0.05m (Threshold: 0.2m)
=========================================
FINAL RESULT: 3/3 TESTS PASSED
=========================================
Ready for submission!
Lab 1: Hello, Robot!
Block 1: Perception

## Slide 11
What to Submit and How to Succeed
Submission Checklist
move_robot.py Your completed script that successfully drives the robot in a 2x2m square.
trajectory.png
The plot generated by
visualize_trajectory.py
showing your robot's path.
check_output.txt
A screenshot or text copy showing that your code
passed all 3 tests in
check_my_lab.py
.
Zip File Format
Package all files into a single zip named
Lab1_YourName_YourID.zip
.
Pro Tips for Success
Read the Comments: The provided code is heavily commented. Read them to understand the why, not just the how.
Test Incrementally: Don't write the whole square at once. Make it move forward first. Then make it turn. Then combine them.
Mind the Units: PyBullet uses meters for distance and radians for angles. (90 degrees = π/2 radians ≈ 1.57).
Use Your Unique Environment:
Always remember to
conda activate robotics_YourName
before running
any scripts.
Lab 1: Hello, Robot!
Block 1: Perception

## Slide 12
You Just Built the Foundation of an Autonomous System
Today you learned to spawn a world, read sensors, command motion, and analyze data. Next week, we give the robot "eyes" with Computer Vision.
Dr. Akram Fatayer
a.fatayer@zuj.edu.jo
linkedin.com/in/akram-fatayer
Lab 1: Hello, Robot!
Al-Zaytoonah University of Jordan